## Slide 1: A Vision Regression Model for Fingertip Aperture Prediction
Saga University Graduate School of Science and Engineering​
Computer Science & Information Techology Course​
Fukuda Laboratory 25742102 DI XIQING
Supervisor: Professor Osamu Fukuda
Notes: Hello everyone im d, my research is ...

## Slide 2
Background
Many hand gesture recognition methods focus on classification.
However, classification alone does not directly describe the continuous changes in finger movements during grasping.
[1] Vásconez, J. P., Barona López, L. I., Valdivieso Caraguay, Á. L., & Benalcázar, M. E. (2022). Hand gesture recognition using EMG-IMU signals and deep q-networks. Sensors, 22(24), 9613.
[2] Zandigohar, M., Han, M., Sharif, M., Günay, S. Y., Furmanek, M. P., Yarossi, M., ... & Schirner, G. (2024). Multimodal fusion of EMG and vision for human grasp intent inference in prosthetic hand control. Frontiers in Robotics and AI, 11, 1312554.
classification 1
classification 2
The Process of Natural Human Grasping
Notes: Approximately 57.7 million people lost an upper limb.
This significantly impacts their daily lives, so the prosthetic hand research aim to help them.
With computational power and algorithms continue to advance, the prosthetic hand are able to recognize an increasing number of movements

## Slide 3
Related Work
Author | Title | Objective | Method
Mangalam et al. | Control of aperture closure during reach-to-grasp movements in immersive haptic-free virtual reality | Investigate factors determine when humans transition from finger opening to closing during object grasping? | Analyze how aperture, hand velocity, and acceleration at the key event - closure onset relate to hand–object distance.
Coats et al. | Predicting the Duration of Reach-to-Grasp Movements to Objects with Asymmetric Contact Surfaces | Investigate how grasping conditions affect movement duration. | Manipulate target distance and fingertip contact surface sizes, and analyze movement time and maximum grip aperture.
These studies demonstrate that reach-to-grasp movements involve multiple interacting variables.
[3] Mangalam, M., Yarossi, M., Furmanek, M. P., & Tunik, E. (2021). Control of aperture closure during reach-to-grasp movements in immersive haptic-free virtual reality. Experimental Brain Research, 239(5), 1651-1665
[4] Coats, R. O., Holt, R. J., Bingham, G. P., & Mon-Williams, M. A. (2018). Predicting the duration of reach-to-grasp movements to objects with asymmetric contact surfaces. Plos one, 13(2), e0193185.
Notes: 1.Vásconez et al. proposed a system, that combine EMG with IMU, adopts a deep reinforcement learning model. Classifies 11 types of grasping movements. The results achieved 97% accuracy. 2.Zandigohar et al. .. This is currently one reason for the high rejection rate of prosthetic hand.

## Slide 4
Research Objective & Question
RQ1
Is there a consistent relationship between hand–object distance and fingertip aperture during reach-to-grasp movements?
RQ2
How accurately can a regression model predict fingertip aperture from hand–object distance during reach-to-grasp movements?
During reach-to-grasp movements, finger opening and closing are coordinated with the hand’s approach to an object.
This study aims to investigate the relationship between hand–object distance and fingertip aperture, and further examine whether a regression model can predict fingertip aperture from hand–object distance in real time.
Notes: So in my research, objective is to Replace classification models to Regression Models. From modular approach to end to end approach to reduce system complexity and loss of important information
RQ is to verify that can the system build on an end-to-end approach combined with regression be successfully applied,

## Slide 5
Experimental Setup
750mm
An overhead web camera captures visual data.
Initial hand position. 30 mm from the object.
30mm

## Slide 6
Example Trial
Camera View:

## Slide 7
Visual Processing
MediaPipe and OpenCV is used to detect hand landmarks and cube
Hand–Object Distance
Distance from the fingertip midpoint to the object center.
Pixels (px)
Hand–Object Distance
Distance from the fingertip midpoint to the object center.
Pixels (px)

## Slide 8
Data Collection
Task: Natural reach-to-grasp movement
Initial hand position: table edge
Target position: 30 mm from the table edge
Target size: 20, 30, and 40 mm cubes
Collect grasping movement data from participants using cubes of different sizes.
Experimental Conditions

## Slide 9
Data Relationship Analysis
30 trial with a 20 mm cube
The data showed high consistency across experiments, suggesting a consistent relationship between hand–object distance and fingertip aperture during reach-to-grasp movements.
Maximum Aperture Timing
44.32 ± 2.37%
Distance at Maximum Aperture (%)
52.15 ± 6.70%
Fingertip Aperture Nomalized RMSE
0.0530 ± 0.0186
Hand–Object Distance Nomalized RMSE
0.0226 ± 0.0112

## Slide 10
Model
Hand–Object
Distance
Fingertip
Aperture
5-frame window MLP
2 hidden layer, each with 32 neurons.
Can fingertip aperture during reach-to-grasp be predicted from hand–object distance?
Loss Function
MAE
Preprocessing
Normalization
Training Data
30 trials

## Slide 11
Offline Validation – Overall Performance
27 validation trials across three cube sizes (9 trials per size)
MAE
3.87
px
RMSE
5.91
px
R²
0.958

## Slide 12
Offline Validation – Phase-Wise Analysis
The grasping phase is the most challenging to predict. However, the current model can reduce prediction errors during this phase.

## Slide 13
Effect of Temporal Window
Comparison between predicted and ground-truth curves, In the red-highlighted region, the model without a temporal window shows poor prediction performance.
Without a temporal window : The model learns only the mapping between distance and fingertip aperture, resulting in larger errors during rapid changes.
With a temporal window:The model can utilize short-term motion context to learn temporal trends, improving prediction accuracy.

## Slide 14
Real-Time Experiment
The model achieved an R² above 0.89 in 8 out of 9 real-time trials, demonstrating promising prediction performance.
Procedure:
Three cubes of different colors and sizes were presented in random order, with three trials per cube.
The system identified the target cube and automatically selected the corresponding trained model for real-time prediction.

## Slide 15
Summary
Future Work
Demonstrated a consistent relationship between hand–object distance and fingertip aperture during reach-to-grasp movements.
Developed a regression model that accurately predicts continuous fingertip aperture from hand–object distance.
Developed a real-time system that automatically selects the appropriate trained model and predicts fingertip aperture in real time.
Conduct grasping experiments with a wider variety of objects.
Recruit additional participants to evaluate the model's generalization ability.

## Slide 16
References
[1] Vásconez, J. P., Barona López, L. I., Valdivieso Caraguay, Á. L., & Benalcázar, M. E. (2022). Hand gesture recognition using EMG-IMU signals and deep q-networks. Sensors, 22(24), 9613.
[2] Zandigohar, M., Han, M., Sharif, M., Günay, S. Y., Furmanek, M. P., Yarossi, M., ... & Schirner, G. (2024). Multimodal fusion of EMG and vision for human grasp intent inference in prosthetic hand control. Frontiers in Robotics and AI, 11, 1312554.
[3] Mangalam, M., Yarossi, M., Furmanek, M. P., & Tunik, E. (2021). Control of aperture closure during reach-to-grasp movements in immersive haptic-free virtual reality. Experimental Brain Research, 239(5), 1651-1665
[4] Coats, R. O., Holt, R. J., Bingham, G. P., & Mon-Williams, M. A. (2018). Predicting the duration of reach-to-grasp movements to objects with asymmetric contact surfaces. Plos one, 13(2), e0193185.