## Slide 1: A Multimodal Fusion-based Shared Control System for Prosthetic Hands Aiming at Unconscious Grasping Adjustment
Saga University
Computer Science & Information Techology
25742102 DI XIQING
Professor Osamu Fukuda

## Slide 2
Background
As the number of executable movements increases, the error rate rises rapidly.
In real-world scenarios, users need to maintain a high level of concentration to achieve control.
As computational power and algorithms continue to advance, prosthetic hand are able to recognize an increasing number of movements.
Problems in real-world usage:
[1] Biddiss, E. A., & Chau, T. T. (2007). Upper limb prosthesis use and abandonment: a survey of the last 25 years. Prosthetics and orthotics international, 31(3), 236-257.
But the rejection rate of prosthetic hands is as high as 40% [1].

## Slide 3
Related Research
Shared control:
Low-level execution is handled autonomously by the system, while the user provides high-level intent.
Marshall et al. used infrared sensors and pressure sensors to develop a shared control algorithm that gradually adjusts the control weighting between the human and the system as the user-controlled prosthetic hand approaches an object [2].
[3] Thomas, N., Miller, A. J., Ayaz, H., & Brown, J. D. (2023). Haptic shared control improves neural efficiency during myoelectric prosthesis use. Scientific reports, 13(1), 484.
[2] Trout, M. A., Mino, F. R., Olsen, C. D., Hansen, T. C., Teramoto, M., Warren, D. J., ... & George, J. A. (2025). Shared human-machine control of an intelligent bionic hand improves grasping and decreases cognitive burden for transradial amputees. Nature Communications, 16(1), 10418.
Thomas et al. focused on achieving precise control of prosthetic grasping force through shared control.
First, the operator manually performs grasping tasks, during which the model learns and records the user’s preferred grasping force as a target value. After this learning phase, the operator only needs to generate a grasping EMG signal, and the prosthetic hand can grasp objects with minimal error relative to the desired force.

## Slide 4
Research Objective
Previous Research
▸ By defining different movements, and based on multimodal sensor data, a neural network is used to ultimately classify them into a single category.
This Research
▸ A regression model is adopted instead of predefining discrete movements; it continuously fine-tunes the output in real time based on feedback from multiple sensors.
focuses on addressing the fine-tuning of hand movements during the object grasping process.
.....

## Slide 5
System Architecture
Fusion
EMG Sensor
Camera
IMU Sensor
Temporal Feature
Temporal Feature
Visual Feature
Output
Opening Width
1 DOF gripper is used to validate the feasibility of the regression model.
Model Training Method - Imitation Learning
The operator manually controls the prosthetic hand.
Record sensors data and hand opening width.
Train the model.

## Slide 6
Objective :
Evaluate the system’s performance, and its ability to reduce the operator’s cognitive load
Participants :
10 healthy adults
Experiment
Scene:
Grasping different size objects under three conditions
Condition A: Manual Control
Condition B: EMG-Only Control
Condition C: Proposed System Control

## Slide 7
Evaluation
Performance
Cognitive load
Task Completion Time
Grasp Success Rate
NASA-TLX [4]
[4] Hart, S. G., & Staveland, L. E. (1988). Development of NASA-TLX (Task Load Index): Results of empirical and theoretical research. In Advances in psychology (Vol. 52, pp. 139-183). North-holland.

## Slide 8
Summary
The objective of research is to reduce the cognitive load of prosthetic users and to address the decline in recognition accuracy caused by an increasing number of movements classes.
The research proposes a multimodal fusion-based shared control system for a prosthetic hand, aiming to achieve unconscious grasping adjustment.
The system employs a regression model that integrates features from EMG, camera, and IMU to continuously and adaptively adjust the hand’s opening width in real time.
Design a comparative experiment to evaluate the effectiveness of the proposed system, using performance and cognitive load as evaluation metrics.

## Slide 9
References
[1] Biddiss, E. A., & Chau, T. T. (2007). Upper limb prosthesis use and abandonment: a survey of the last 25 years. Prosthetics and orthotics international, 31(3), 236-257.
[2] Trout, M. A., Mino, F. R., Olsen, C. D., Hansen, T. C., Teramoto, M., Warren, D. J., ... & George, J. A. (2025). Shared human-machine control of an intelligent bionic hand improves grasping and decreases cognitive burden for transradial amputees. Nature Communications, 16(1), 10418.
[3] Thomas, N., Miller, A. J., Ayaz, H., & Brown, J. D. (2023). Haptic shared control improves neural efficiency during myoelectric prosthesis use. Scientific reports, 13(1), 484.
[4] Hart, S. G., & Staveland, L. E. (1988). Development of NASA-TLX (Task Load Index): Results of empirical and theoretical research. In Advances in psychology (Vol. 52, pp. 139-183). North-holland.