## Slide 1: An End-to-End Multimodal Fusion-based Shared Control System for Prosthetic Hands Aiming at Unconscious Grasping Adjustment
Saga University
Computer Science & Information Techology
25742102 DI XIQING
Professor Osamu Fukuda

## Slide 2
Background
57.7 million people in world
who had lost an upper limb [1]
Computational power and algorithms continue to advance, the prosthetic hand are able to recognize an increasing number of movements [2]

## Slide 3
Related Research
Vásconez et al. proposed
EMG + IMU
Deep reinforcement learning model
11 movements
accuracy: 97% [3]
Zandigohar et al. proposed
EMG + Eyes Tracking
Extra-Trees and YOLOv4
14 movements
accuracy: 93% [4]

## Slide 4
Research Gap
Cognitive Load
But the rejection rate of prosthetic hands is as high as 44% [5].
Modular Pipeline
Modular Pipeline will increases system complexity but also may lead to the loss of important information.
Users need to maintain a high level of concentration to achieve control.
Movement Transition
Transitions and adjustments between movements were not considered.

## Slide 5
Research Novelty
Replace the classification model with a regression model to enable real-time dynamic adjustment.
1
2
3
End-to-end training directly uses raw signals, without separate EMG and other modules.
Shared control delegates fine movement control to the system, reducing user cognitive load.

## Slide 6
System Architecture
Fusion
EMG Sensor
Camera
IMU
Temporal Feature
Temporal Feature
Visual Feature
Output
Opening Width
1 DOF gripper is used to validate the feasibility of the regression model.
Model Training Method - Imitation Learning
The operator manually controls the prosthetic hand.
Record sensors data and hand opening width.
Train the model.
Neural Network

## Slide 7
Objective :
Evaluate the system’s performance, and its ability to reduce the operator’s cognitive load
Participants :
10 healthy adults
Experiment
Scene:
Grasping different size objects under three conditions
Condition A: Manual Control
Condition B: EMG-Only Control
Condition C: Proposed System Control

## Slide 8
Evaluation
Performance
Cognitive load
Task Completion Time
Grasp Success Rate
NASA-TLX [6]

## Slide 9
Summary
The objective of research is to address real-time adjustment of the prosthetic hand and reduce the cognitive load of prosthetic users.
The System Adopts an end-to-end approach without modular separation.
Employs a regression model to continuously adjust the hand’s opening width in real time.
Employs a multimodal fusion-based shared control approach for the prosthetic hand.
Design a comparative experiment to evaluate the feasibility of the proposed system, using performance and cognitive load as evaluation metrics.

## Slide 10
References
[1] McDonald C L, Westcott-McCoy S, Weaver M R, et al. Global prevalence of traumatic non-fatal limb amputation[J]. Prosthetics and orthotics international, 2021, 45(2): 105-114.
[2] Chen, Z., Min, H., Wang, D., Xia, Z., Sun, F., & Fang, B. (2023). A review of myoelectric control for prosthetic hand manipulation. Biomimetics, 8(3), 328.
[3] Vásconez, J. P., Barona López, L. I., Valdivieso Caraguay, Á. L., & Benalcázar, M. E. (2022). Hand gesture recognition using EMG-IMU signals and deep q-networks. Sensors, 22(24), 9613.
[4] Zandigohar, M., Han, M., Sharif, M., Günay, S. Y., Furmanek, M. P., Yarossi, M., ... & Schirner, G. (2024). Multimodal fusion of EMG and vision for human grasp intent inference in prosthetic hand control. Frontiers in Robotics and AI, 11, 1312554.
[5] Salminger, S., Stino, H., Pichler, L. H., Gstoettner, C., Sturma, A., Mayer, J. A., ... & Aszmann, O. C. (2022). Current rates of prosthetic usage in upper-limb amputees–have innovations had an impact on device acceptance?. Disability and rehabilitation, 44(14), 3708-3713.
[6] Hart, S. G., & Staveland, L. E. (1988). Development of NASA-TLX (Task Load Index): Results of empirical and theoretical research. In Advances in psychology (Vol. 52, pp. 139-183). North-holland.