## Slide 1
3D Surface Plot
Data Line Chart
3
A Multimodal Fusion-Based Prosthetic Hand Control System via Natural Grasping
Most current prosthetic hands rely on preset pattern recognition — once a grasp category is identified, no further adjustment is made. This study records data from natural human grasping to analyze the relationship between target size, velocity, and finger width, providing a predictive basis for the prosthetic hand to mimic human grasping behavior.
タスク
Record data from natural human grasping and build a dynamic model of human grasping to learn this process, with the goal of predicting finger width during grasping.
Objective
The data collection system uses a camera and IMU to synchronous-ly record grasping velocity,
target object area, and
finger width.
System
Finger width consistently shows a rise–peak–close pattern and changes with target area and velocity. The same pattern appears across different object sizes.
Result
Record Grasping Process
Recording Device