## Slide 1
Research Objective & Question
RQ1
Is there a consistent relationship among object apparent size, fingertip aperture, and hand acceleration during reach-to-grasp movements?
RQ2
Can fingertip aperture during reach-to-grasp movements be predicted using object apparent size and hand acceleration?
During reach-to-grasp movements, finger opening/closing and hand motion are usually coordinated naturally and unconsciously.
This study aims to investigate the relationship among object apparent size, fingertip aperture, and hand acceleration during grasping, and further examine whether this information can be used to predict the fingertip aperture process.
Notes: So in my research, objective is to Replace classification models to Regression Models. From modular approach to end to end approach to reduce system complexity and loss of important information
RQ is to verify that can the system build on an end-to-end approach combined with regression be successfully applied,

## Slide 2
Data Collection
Task: natural reach-to-grasp movement
Initial hand position: table edge
Target position: 30 mm from the table edge
Target size: 20, 25, 30, 35, 40, and 45 mm cubes
Equipment : A recording device consisting of a web camera and an IMU was mounted on the participant's forearm.
Collect participants grasping data for objects of different sizes.
Experimental Conditions
Web Camera (30hz)
50hz

## Slide 3
Data Relationship Analysis
20 experiments with a 40 mm object
Object apparent size
Normalized RMSE
0.0486 ± 0.0313
Object apparent size Normalized RMSE
0.0757 ± 0.0294
Fingertip aperture Normalized RMSE
0.0415 ± 0.0160
Maximum aperture timing
55.79 ± 2.45%
Object area at maximum aperture / final object area
59.42 ± 4.15%
Mean acceleration during opening
0.611 ± 0.139 m/s²
The data showed high consistency across experiments, suggesting a consistent relationship among object apparent size, fingertip aperture, and hand acceleration during reach-to-grasp movements.

## Slide 4
Model
Further validation
Acceleration
Object Size
Fingertip
Aperture
Can fingertip aperture during reach-to-grasp movements be predicted using object apparent size and hand acceleration?
15-frame window MLP
20, 30, 40 mm: 15 training experiments + 5 test experiments
25, 35, 45 mm: 5 experiments for generalization testing

## Slide 5
Standard Test

## Slide 6
Generalization Test

## Slide 7
Generalization Test

## Slide 8
Generalization Test

## Slide 9
Generalization Test

## Slide 10
Generalization Test